## Slide 1: Principles of motion economy
The principles of motion economy form a set of rules and suggestions to improve the manual work in manufacturing and reduce fatigue and unnecessary movements by the worker, which can lead to the reduction in the work related trauma.
The principles of motion economy can be classified into four groups
Principles related to the use of human body,
Principles related to the arrangement of the work place,
Principles related to the design of tools and equipment.
Principles related to time conservation.

## Slide 2: The use of human body
Both hands should be fully utilized.
The two hands should begin motions at the same time.
The two hands should not be idle at the same time except during rest periods.
The motions of the hands and arms should be symmetrical and simultaneous.
The method should be designed to utilize the worker’s feet and legs when appropriate.
Five Classifications of Hand and Arm Motions are:
Finger motions
Wrist motions
Forearm motions
Upper arm motions
Shoulder motions

## Slide 3: Classifications of Hand and Arm Motions

## Slide 4: Arrangement of the Work Place
There should be a definite and fixed place for all tools and materials.
Locate tools and materials in fixed positions within the work area
Locate tools and materials close to where they are used
Materials and tools should be located to permit the best sequence of motions.
Arrange the height of the workplace and chair for alternate sitting and standing, when possible.
Provide a chair of the type and height to permit good posture.

## Slide 5: Arrangement of the Work Place
Provide a chair of the type and height to permit good posture.

## Slide 6: Arrangement of the Work Place
The following figure shows the normal and maximum working areas in the workplace.

## Slide 7: Arrangement of the Work Place
Normal and Maximum Working Area Dimensions in Figure Above

## Slide 8: Two workplace layouts:
(a) Poor arrangement of parts and tools in workplace.

## Slide 9: Two workplace layouts:
(b) Good arrangement of parts and tools in workplace Numbers indicate sequence of work elements in relation to locations of hand tools and parts bins.

## Slide 10: Design of Tools and Equipment
Combine multiple functions into one tool where possible
Preposition tools and materials.
Where each finger performs some specific movement, the load should be distributed in accordance with the inherent capacities of the fingers.
Perform multiple operations simultaneously rather than sequentially.
Design equipment controls for operator convenience and error avoidance.
Hand tools and portable power tools should be designed for operator comfort & convenience.
Mechanize or automate manual operations if economically and technically feasible.

## Slide 11: Time Conservation
Even a temporary delay of work by a man or machine should not be encouraged.
Machine should not run idle, it is not desirable that a lathe machine is running and its job is rotating but no cut is being taken.
Two or more jobs should be worked upon at the same time or two or more operations should be carried out on a job simultaneously if possible.
Number of motion involved in completing a job should be minimized.

## Slide 12: Benefits of Motion Economy
The benefits of motion economy includes:
It grows the ability of workers due to the application of good methods, using of good tools and eliminating unnecessary activities.
Extended life of machines.
Reduces exhaustion of workers.
Decreases labor costs due to less wastage in factories or plants.