## Slide 1: Work Study and Method Engineering Lab-1

## Slide 2: What is Method Engineering?
A branch of industrial engineering specializing in the analysis of methods and the improvement and standardization of methods, equipment, and working conditions
Methods engineering is the analysis and design of work methods and systems, including the tooling, equipment, technologies, workplace layout, plant layout, and work environment
Other names for methods engineering:
  Work study
  Work simplification
  Methods study
  Process re-engineering
  Business process re-engineering

## Slide 3: Methods Engineering
Can be divided into two areas:
Methods analysis and Methods design.
Methods analysis is concerned with the study of an existing method or process.
Objectives:
  Eliminate unnecessary and non-value-adding work elements
  Combine elements and operations
  Rearrange elements into more logical sequence
  Simplify remaining elements and operations

## Slide 4
Methods design is concerned with either of the following situations:
  Design of a new method or process
    Required for new product or service and there is no existing standard
  2. Redesign of an existing method or process based on a previous methods analysis.

## Slide 5: Objectives of Method Engineering?
The improvement of processes and procedures.
The improvement of plan, office or service area layout.
Economy in human effort and the reduction of unnecessary fatigue.
Improvement in the use of materials, machines and manpower.
Development of a better physical working environment.

## Slide 6: HOW TO APPLY METHODS ENGINEERING
Systematic Approach in Methods Engineering
The systematic approach in methods engineering consists of the steps described below.
  Step 1: Define the Problem and Objectives. The problem in methods engineering study may be low productivity, high cost, inefficient methods, or the need for a new method or a new operation. The objective is the desired improvement or new methods design. Possible objectives are to increase productivity, reduce labor content and cost, improve safety, or develop a new method or new operation.

## Slide 7
Step 2: Analyze the Problem. Data collection and analysis activities for the type of problem being studied.
Activities often used in this step include the following:
  Identify the basic function of the operation.
  Gather background information.
  Observe the existing process or observe similar processes if the problem involves a new work design.
  Collect data on the existing operation and document the details in a format that provides itself to examination.
  Conduct experiments on the process.

## Slide 8
  Step 3: Formulate Alternatives. There are always multiple ways to perform a task or accomplish a process, some of which are more efficient and effective than others.
  The purpose of this step in the problem-solving approach that is not to identify the best alternative but to formulate all of the alternatives that are feasible.
Step 4: Evaluate Alternatives and Select the Best. This step consists of a systematic assessment of the alternatives and the selection of the best solution among them, based on the original definition of the problem and objectives.

## Slide 9
Step 5: Implement the Best Method. Implementation means installing the selected solution: introducing the changes proposed in the existing method or operation, or installing the new method or process.
  This may involve pilot studies or trials of the new or revised
  Implementation also includes complete documentation of the new or revised method and replacement of the previous documentation
Step 6: Audit the Study. Perform an audit or follow-up on the methods engineering project.
  How successful was the project in terms of the original problem definition and objectives?
  What were the implementation issues?
  What should be done differently in the next methods engineering study?
For an organization committed to continuous improvement, answers to these kinds of questions help to fine-tune its problem-solving and decision-making skills.

## Slide 10: Differentiate between time, motion and method study

## Slide 11: Differentiate between time, motion and method study
BASIS FOR COMPARISON | TIME STUDY | MOTION STUDY
Meaning | Time study is one of the techniques of scientific management which involves observation and recording of the time taken in performing a particular task. | Motion study involves the observation of the movement of men, machine, materials and supplies, to find out the wasteful actions and eliminate them.
Involves | Tracking of the time consumed in carrying each part of the operation. | Ascertainment of total movements of workers while performing a task.
Purpose | To identify the standard time required to perform a task. | To reduce wastage of time and energy in unnecessary movements.
Tools used | Stopwatch | Surveillance Camera
Focuses on | Increase in productivity of labour. | Minimization of movement of workers.
Objective | To determine a fair day's work. | To find out the best method of doing a job.

## Slide 12: History
Frank Bunker Gilbreth (July 7, 1868 – June 14, 1924) was an American engineer, consultant, and author known as an early advocate of scientific management and a pioneer of time and motion study,
Both he and his wife Lillian Moller Gilbreth were industrial engineers and efficiency experts who contributed to the study of industrial engineering in fields such as motion study and human factors.
Frank and Lillian Gilbreth wrote some of the original work that laid the foundation for the field of motion and time study. They were the pioneers of motion study.

## Slide 13: History
Frederick Taylor (July 7, 1868 – June 14, 1924) was an American inventor that established the Scientific Management Theory or Taylorism to influence how work was performed using scientific techniques.
Taylor was trained as an engineer by undertaking a master's degree in mechanical engineering.
To enhance his theory, Frederick Taylor wrote books like Shop Management and The Principles of Scientific Management.
Through those books, Taylor impacted management through quantitative concepts like cost accounting, ergonomics, and assembly line production to apply science to conduct quantitative analysis.

## Slide 14: History
The Fredrick Taylor theory explained that the optimization of work translated to productivity and efficiency and not how the workers were made to work hard.
The Taylor scientific management theory assumed that productivity could increase by making jobs simpler and optimizing them.

## Slide 15: History
The four principles of Scientific Management are as follows:
Splitting work between workers and managers where workers would create plans and workers would follow them.
The scientific training and hiring of workers.
The collecting of data and its analysis reduced to rules and laws.
Monitoring worker performance.

## Slide 16: History